## Slide 1
Presented by:
EZZARA Abderrahim
Authors:
Pr. AYAD Hassan
Pr. OUADINE Ahmed Youssef
Mr. EZZARA Abderrahim
Sliding Mode Active Fault-Tolerant Control for Quadrotor UAV System in Presence of Actuator Faults
Department of Applied Physics
Faculty of Science and Technology, CADI AYYAD university
Marrakesh, Morocco
Notes: Hello, everyone.
My name is Ezzara Abderrahim, and I am a PhD student in LSEEET Laboratory, Department of Applied Physics in the Faculty of Science and Technology, CADI AYYAD university, Marrakesh, Morocco. Actually, working on fault-tolerant control for autonomous vehicles.
Today, I'm looking to present a new technique for "Adaptive Observer-based Fault-Tolerant Control for Actuator Faults in Quadrotor UAVs."
Thank you for joining me today.

## Slide 2
Fault Tolerant Control (FTC)
Faults sources
Wear and Tear;
Mechanical Damage;
Environmental Factors;
Electrical Issues;
Traditional Methods
Struggle to handle unexpected issues;
Typically designed to work under ideal conditions;
Quadrotor may become unstable, deviate from its intended path, or even crash;
01
Problem statement
FTC is a type of control system to maintain the stability and performance of a system even when faults occur.

## Slide 3
FTC Structure
Adaptive observer: Estimate the actuator faults
Sliding mode controller: Adjusts the control strategy
Proposed FTC
02
Quadrotor
Adaptive observer
Sliding mode Controller
FTC Bloc
Actuator Faults
Desired path
Estimated faults
Notes: Many actuator-fault-tolerant control strategies have been proposed, mainly based on observer-based techniques. Using adaptive observers, it is possible to estimate faults that are represented as changes in parameters.
Unfortunately, The observer matching condition is not satisfied for our system. Therefore we cannot use the standard adaptive observer form.
The proposed FTC technique uses the backstepping technique to synthesize the control laws, taking into account the real-time faults estimated by an adaptive observer that satisfy the cited condition.

## Slide 4
Outline
Quadrotor Nonlinear Dynamical modeling
Nonlinear adaptive observer design
Quadrotor FTC in presence of Actuator Faults
Simulation Results
Conclusion
03
03
Notes: The first part of this presentation is : Quadrotor Nonlinear Dynamical modeling

## Slide 5
E (O, X, Y, Z) designate an inertial frame.
B (o, x, y, z) a frame permanently coupled to the quadrotor body.
The absolute position
The attitude by the three Euler’s angles .
Fig. 1. Quadrotor configuration
Nonlinear Dynamical model
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
04
E
Notes: In order to establish the quadrotor model, we will need two reference frames. Let E (O, X, Y, Z) designate an inertial frame, and B (O, x, y, z) designate a frame permanently coupled to the quadrotor body, as illustrated in figure 1.
The absolute position of the quadrotor may be obtained by the three coordinates and its attitude by the three Euler’s angles, respectively:
roll angle (rotation around the x-axis)
pitch angle (rotation around the y-axis)
and yaw angle (represent the rotation around the z-axis).

## Slide 6
is the resultant of the forces generated by the four rotors
the resultant of the drag forces along (X,Y,Z) axis
is the moment developed by the quadrotor
is the resultant of aerodynamics frictions torques
is the resultant of torques due to the gyroscopic effects
Attitude coordinates
Position coordinates
Torques
Moment
Forces
Newton-Euler formalism
is the gravity force
The quadrotor dynamical model can be derived using the Newton-Euler formalism.
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
05
Notes: The quadrotor dynamical model can be derived using the Newton-Euler formalism.
Various physical phenomena that might impact its dynamics are taken into account, for example:
The forces generated by the four rotors.
The drag forces along (X,Y,Z) axis.
The gravity force.
The moment developed by the quadrotor.
The resultant of aerodynamics frictions torques.
The resultant of torques due to the gyroscopic effects.
Using Newton-Euler formalism and taking in to account these forces, moments and torques, we can extract the attitude and the position coordinates of the quadrotor.

## Slide 7
The quadrotor's dynamic model:
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
06
Notes: The quadrotor's dynamic model, is given by these equations, where :
, , , and represent the control inputs of the system
The quadrotor's dynamic model, is given by these equations, where :
𝑈_1, 𝑈_2, 𝑈_3, and 𝑈_4 represent the control inputs of the system.
𝐼_𝑥, 𝐼_𝑦 and 𝐼_𝑧 are the constants inertia.
𝐾_𝑓𝑡𝑥, 𝐾_𝑓𝑡𝑦and 𝐾_𝑓𝑡𝑧 are the translation drag coefficients.
𝐾_𝑓𝑎𝑥, 𝐾_𝑓𝑎𝑦and 𝐾_𝑓𝑎𝑧 are the aerodynamic friction coefficients around x, y, and z.

## Slide 8
Outline
Quadrotor Nonlinear Dynamical modeling
Nonlinear adaptive observer design
FTC Strategy of Quadrotor in presence of Actuator Faults
Simulation Results
Conclusion
07
Notes: Let us now move to the second part : Nonlinear adaptive observer design

## Slide 9
4
5
6
1
2
3
The pair (, ) is observable.
Given that is bounded, the first derivative of in time is both continuous and bounded.
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
08
The complete model may be expressed in state-space form:
and satisfy the Lipschitz property with respect to .
is the state vector of the system.
is the output vector.
represent the actuator faults vector.
, , and are known constant matrices.
and known nonlinear functions
Notes: The complete model may be expressed in state-space form as below.
The following assumptions are considered:
The first assumption: The pair (, ) is observable;
The second assumption: and satisfy the Lipschitz property with respect to .
thirdly : The fault vector is bounded in the following sense:
Assumption number four: The actuator faults are piecewise constant and slowly vary in time as follows:
The fifth assumption: System matrices satisfy the following condition
The last assumption: Given that is bounded, the first derivative of in time is both continuous and bounded.
The following assumptions are considered:
The first assumption: The pair (𝐶, 𝐴) is observable;
The second assumption: Ф(𝑥,𝑢) and 𝜎(𝑥) satisfy the Lipschitz property with respect to 𝑥.
The thirdly : The fault vector 𝑓_𝑎 is bounded in the following sense:
Assumption number four: The actuator faults are piecewise constant and slowly vary in time as follows:
The fifth assumption: The matrices 𝐴, 𝐵, 𝐸 and 𝐶 satisfy
The last assumption: Given that 𝑥 is bounded, the first derivative of 𝜎(𝑥) in time is both continuous and bounded.

## Slide 10
Coordinate change
New system
Original system
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
09
Adaptive observer representation
Notes: Define new coordinates as , where
The original system takes the following form in the new coordinate system:
Based on the new system state space representation, we suggest the following adaptive observer:
Then, both the system state and the actuator faults can be simultaneously estimated by the adaptive observer
Define new coordinates as 𝑧 = 𝑇 𝑥, where
The original system takes the following form in the new coordinate system:
Based on the new system state space representation, we suggest the following adaptive observer:
Then, both the system state and the actuator faults can be simultaneously estimated by the adaptive observer

## Slide 11
If the above assumptions are satisfied the observation error is asymptotically stable, and the fault estimation error remains bounded, such that:
Theorem 1
1
2
3
LMI optimization
(Simultaneous solve of 1, 2 and 3 )
1
2
3
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
10
, and
And and
Notes: Theorem 1 provides a strategy to design an adaptive observer using a LMI formulation.
Once the previous conditions are satisfied, the observer gain L is selected as
The vector converges to zero.
Theorem 1 provides a strategy to design an adaptive observer using a LMI formulation.
Once the previous conditions are satisfied, the observer gain L is selected as
The vector 𝑒_𝑓 converges to zero.

## Slide 12
Quadrotor
Adaptive
observer
Nonholonomic constraints
U1
U4
Ux
Uy
U2
U3
Real faults
Estimated faults
Fault tolarent controller
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
11
An active fault-tolerant tracking control system approach for actuator faults.
Notes: By adding this adaptive observer, our complete fault tolerant control strategy is given by the following scheme.
In this structure the adaptive observer allows to estimate the actuator faults.
These estimates are then taken into account by the control laws to form an active fault tolerant control.

## Slide 13
Outline
Quadrotor Nonlinear Dynamical modeling
Nonlinear adaptive observer design
Quadrotor FTC in presence of Actuator Faults
Simulation Results
Conclusion
12
Notes: Let us go to the third part : Quadrotor Fault Tolerant Control in presence of Actuator Faults

## Slide 14
An iterative algorithm is employed to synthesize the control laws.
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
13
1
2
3
control laws
SMC Approach
(Find such that )
where
Notes: The SMC technique is used to generate control laws leading the system to follow the desired path in the normal and the faulty case.
is the tracking error
is the sliding surfaces
are the Lyapunov functions
Using the backstepping approach, we can extract control laws ()
Based on the backstepping technique, an iterative algorithm is employed to synthesize the control laws leading the system to follow the desired path in the normal and the faulty case.
𝑒_𝑖 is the tracking error
𝑒_𝑧 is the observation error
𝑒_𝑓 is the fault estimation error
The related Lyapunov functions are provided by:
Using the backstepping approach, we can extract control laws (𝑈_1,𝑈_2,𝑈_3,𝑈_4, 𝑈𝑥 𝑎𝑛𝑑〖 𝑈〗_𝑦)

## Slide 15
The synthesized stabilizing control laws are as described in the following:
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
14
Notes: This command benefits from the SMC properties, such as robustness,
and it allows a real time fault compensation because it takes into account the estimated faults.

## Slide 16
Outline
Quadrotor Nonlinear Dynamical modeling
Nonlinear adaptive observer design
Quadrotor FTC in presence of Actuator Faults
Simulation Results
Conclusion
15
Notes: Let us pass to the fourth section : Simulation Results

## Slide 17
We executed simulations in MATLAB/SIMULINK® environment.
The quadrotor object of our study is the Draganfly IV, manufactured by Draganfly Innovations.
Two actuator faults related to are introduced.
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
16
Notes: In order to evaluate the performance and effectiveness of the proposed approach, we executed simulations in MATLAB/SIMULINK® environment.
The LMIs were solved using CVX, a MATLAB-based modeling system for convex optimization.
The quadrotor object of our study is the Draganfly IV, manufactured by Draganfly Innovations.
Two actuator faults related to are introduced.
In order to evaluate the performance and effectiveness of the proposed approach, we executed simulations in MATLAB/SIMULINK® environment.
The LMIs were solved using CVX, a MATLAB-based modeling system for convex optimization.
The quadrotor object of our study is the Draganfly IV, manufactured by Draganfly Innovations.
In this simulation test, four actuator faults related to roll, pitch, yaw, and altitude (𝜑, 𝜃, 𝜓, 𝑧) are introduced.

## Slide 18
The estimated states converge to the real ones accurately before and after the fault occurrence.
A. States estimation
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
17
Fig. 2. Trajectories over roll (𝜑), pitch (θ), yaw angle (ψ), and altitude (z)
Desired state
Traditional SMC
FTC-SMC
Notes: The state estimates in the faulty case are shown in Figure 2.
It can be seen that the real states converge to the desired ones even in the presence of faults,
which clearly illustrates the good performance and robustness of the control strategy.

## Slide 19
The estimated states converge to the real ones accurately before and after the fault occurrence.
A. States estimation
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
18
Fig. 3. Trajectories over roll (𝜑), and altitude (z)
Desired state
Traditional SMC
FTC-SMC
Notes: Let's zoom in on the roll (𝜑) and altitude (z) states affected by faults.

## Slide 20
Convergence time of less than 1 second, ensuring fast fault detection.
B. Fault estimation
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
19
Fig. 4. Fault estimation
Notes: The convergence time of less than 1 second ensures rapid fault detection.
The RMSE of for , and for , indicates precise fault estimation
Therefore, the proposed observer can give a fast and accurate fault estimation.
Figure 3 presents the true and estimated faults.
According to this figure, there is a very excellent estimation of the actuator faults and the mean of the estimation error is of the order of 10^(−7).
Therefore, the proposed observer can give a fast and accurate fault estimation.

## Slide 21
Excellent performance and resilience towards stability and tracking despite the occurrence of actuator failures.
Fig.5. The quadrotor's global trajectory in 3D
C. The quadrotor's global trajectory in 3D
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
20
Notes: Figure 5 presents the 3D location of the quadrotor in the faulty scenario.
It demonstrates excellent performance and resilience towards stability and tracking despite the occurrence of actuator failures.

## Slide 22
Fig.7. Control inputs of actuators in faulty case
D. Estimation errors
Fig.6. Tracking errors
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
21
E. Control inputs
Traditional SMC
FTC--SMC
The input control signals are acceptable and physically realizable.
 | [rad] | [m]
Traditional SMC |  | 
FTC-SMC |  | 
Traditional SMC |  | 
FTC-SMC |  | 
Notes: The SMC-based FTC method shows significant improvements over traditional SMC. This demonstrates the enhanced precision and fault tolerance of the proposed approach.
The input control signals are acceptable and physically realizable.
The estimation errors (Figure 5) quickly converge to 0 and remain below 10^(−3).
The roll (φ), pitch (θ) and yaw (ψ) estimation errors remain close to zero (≈10^(−3)).
The attitude estimation error remains 2% of the desired attitude.
Despite the faults, we can conclude that the trajectory tracking of our system is assured.

## Slide 23
Outline
Quadrotor Nonlinear Dynamical modeling
Nonlinear adaptive observer design
Quadrotor FYC in presence of Actuator Faults
Simulation Results
Conclusion
22
Notes: we end with conclusion

## Slide 24
FTC Strategy
Adaptive observer
Dynamical modeling
Simulation Results
Conclusion
23
The contributions of this work
Both system state and the actuator faults can be simultaneously estimated by the used AO.
The used observer does not require that the system structure meets the required standard observer matching requirement for the traditional ASO.
RMSE values in the faulty case less than .
Regardless of the number of tracked outputs, both additive and multiplicative faults can be estimated.
The non-linearity of the quadrotor and the high-order non-holonomic constraints are not neglected.
It made it possible to precisely estimate the faults and ensure stability and trajectory tracking using an LMI optimization problem.
1
2
3
4
5
6
Notes: The non-linearity of the quadrotor and the high-order non-holonomic constraints are not neglected.
Both system state and the actuator faults can be simultaneously estimated by the used AO.
The used observer does not require that the system structure meets the required standard observer matching requirement for the traditional ASO.
Regardless of the number of tracked outputs, both additive and multiplicative faults can be estimated.
RMSE values in the faulty case less than .
It made it possible to precisely estimate the faults and ensure stability and trajectory tracking using an LMI optimization problem.
The non-linearity of the quadrotor and the high-order non-holonomic constraints are not neglected.
Both system state and the actuator faults can be simultaneously estimated by the used AO.
The used observer does not require that the system structure meets the required standard observer matching requirement for the traditional ASO.
Regardless of the number of tracked outputs, both additive and multiplicative faults can be estimated.
The simulation results have proven the significant accuracy of this control approach, with the mean estimate error of the order of 10^(−7).
It made it possible to precisely estimate the faults and ensure stability and trajectory tracking using an LMI optimization problem.

## Slide 25
Thank you for your attention
Sliding Mode Active Fault-Tolerant Control for Quadrotor UAV System in Presence of Actuator Faults

## Slide 26
Presented by:
EZZARA Abderrahim
Authors:
Pr. AYAD Hassan
Pr. OUADINE Ahmed Youssef
Mr. EZZARA Abderrahim
Sliding Mode Active Fault-Tolerant Control for Quadrotor UAV System in Presence of Actuator Faults
Department of Applied Physics
Faculty of Science and Technology, CADI AYYAD university
Marrakesh, Morocco
Notes: Hello, everyone.
My name is Ezzara Abderrahim, and I am a PhD student in LSEEET Laboratory, Department of Applied Physics in the Faculty of Science and Technology, CADI AYYAD university, Marrakesh, Morocco. Actually, working on fault-tolerant control for autonomous vehicles.
Today, I'm looking to present a new technique for "Adaptive Observer-based Fault-Tolerant Control for Actuator Faults in Quadrotor UAVs."
Thank you for joining me today.

## Slide 27
Annex

## Slide 28
Parameters
C and S represent the trigonometrical functions cosines and sines respectively.
is the total mass of the quadrotor.
is the gravity acceleration constant.
is the drag coefficient.
, and are the constants inertia.
, and are the translation drag coefficients.
, and are the aerodynamic friction coefficients around x, y, and z.
is the distance between the quadrotor center of mass and the rotation axis of propellers.
is the rotor inertia.
is the disturbance due to the rotor imbalance.
, , , and represent the control inputs of the system.

## Slide 29
Based on the angular speeds of the four rotors, the control inputs and the disturbance are expressed as follows:
 | (2)
 | (3)
 | (2)
 | (3)

## Slide 30
 | (16)
 | (16)
The state space correspondent to the model (1) is rearranged as follow:
And